Effect of Magnetic Field on Unsteady MHD Poiseuille Flow of a

Third Grade Fluid under Exponential Decaying

Pressure Gradient with Ohmic Heating

1*Lawal O. W., 2Ali Y. K. and 2Lukman A. O.

1.	Department of Mathematics, Tai Solarin University of Education Ijagun, Ogun State, Nigeria

2.    Department of Mathematics and Statistics Hassan Usman Katsina Polytechnnic Katsina State Nigeria

# * E-mail of the corresponding author: waheedlawal207@yahoo.com

Abstract

The unsteady MHD Poiseuille flow of a third grade fluid between two parallel horizontal non conducting porous plates is studied with heat transfer. The two plates are fixed but maintained at different constant temperature with the Joule and viscous dissipation taken into consideration. The fluid motion is produced by a sudden uniform exponential decaying pressure gradient and external uniform magnetic field that is perpendicular to the plates.

The governing momentum and energy equation arise from the flow are solved numerically using Maple program. The effects of magnetic field and third grade parameter on velocity and temperature profile are examined through several graphs.

Keyword:- Poiseuille flow, MHD flow, Third grade fluid, Maple software, Exponential Decaying Pressure Gradient, Heat transfer.

1.  Introduction

The study of the flow of a third grade fluid between two parallel plates subjected to magnetic field has received considerable attention in the past decades due to its applications in industry and engineering. Some of these applications can be found in materials manufactured by extraction process especially in polymer processing, micro fluids, geological flows within the earth’s mantle, the flow of synovial fluid in human joints as well as in the drilling of oil and gas well.

Several researchers have successfully analysed the flow of third grade fluid between two parallel plates. Hayat et al [1] analysed the steady flow and heat transfer characteristics of a third grade fluid between two porous plates. They investigated three flow problems [namely: plane couette flow, plane poiseuille flow and plane couette poiseuille flow] and analytically expressed the velocity and temperature profile for each case.

Siddique et al [2] study unsteady flow of an incompressible Oldroyd – B fluid between two infinite parallel plates when the slippery between the plate and fluid is valid. They obtained analytical solutions of the problems and show the effects of various dimensionless parameters emerging from the governing equation on velocity field. The effects of magnetic field on the MHD flow of third grade fluid through inclined channel with heat transfer were carried out by Aiyesimi et al [3]. The non-linear differential equations governing the flow and heat transfer are solved by employing the regular perturbation technique and the results are presented graphically. Nayak et al [4] gave numerical solution for the flow and heat transfer of a third grade fluid past a porous vertical plate.

In all these mentioned studies the pressure gradient was neglected. In this work, the MHD flow of a third grade fluid between two parallel horizontal porous plates is studied with the consideration of heat transfer. A sudden uniform and an exponential decaying pressure gradient, an external uniform magnetic field that is perpendicular to the plates and uniform suction and injection through the surface of the plates are applied. By assuming a very small magnetic Reynolds number [5], the induced magnetic field is neglected. The two plates are kept at two different constant temperatures. The governing non linear partial differential equations involved are solved numerically using a computer program generated by Maple software.

2.  Formulation of the Problem

We consider incompressible non Newtonian third grade fluid flowing through infinite parallel plates of distant  apart. The upper and lower plates are located at  planes and extend from. The two plates are kept stationary and maintained at two different but constant temperature with upper plate simultaneously subjected to a steady change in temperature  . The flow is driven by a uniform and exponential decaying pressure gradient  in the - direction, and a uniform suction from the above and injection from below which are applied at . A uniform magnetic field  is applied in positive - direction and is assumed undisturbed as the induced magnetic field is neglected under the assumption of small magnetic Reynolds number. The plates are assumed to be infinite in the  and directions which makes the physical quantities do not change in these directions.

Therefore we seek a velocity vector of the fluid as

(1)

where  is the main velocity component in the direction while  indicates suction velocity which is assumed to be constant in direction.

The boundary and initial conditions are  for (since there is non-slip condition at the plates) and  respectively.

For the temperature of the fluid, the boundary and initial conditions are ,  for  at  respectively.

The fundamental equations governing the unsteady MHD flow of a third fluid are the continuity equation

(2)

and momentum equation

(3)

where  is the density of the fluid,  is the fluid velocity,  is the magnetic induction. So that  are applied and induced magnetic field respectively) and

(4)

is the current density  is the electrical conductivity,  is the electrical field which is not considered ,  denote the material derivative,  is the pressure,  is the external body force and  is the Cauchy stress tensor which for a third grade fluid satisfies the constitutive equation

(5)

(6)

where  is the Isotropic stress due to constraint incompressibility,  is the dynamics viscosity,   are the material constraints,  indicates the matrix transpose  are the first three Rivlin Ericksen tensor and   is the identity tensor [7].

Since the flow is driven by a uniform and exponential decaying pressure gradient equation (1) – (6) yield

(7)

The temperature profile is governed by the energy equation [8]

(8)

where and  are respectively specific heat capacity and thermal conductivity of the fluid.

Let us introduce the following dimensionless variables and parameters

is the Reynolds number

is the second grade parameter

is the third grade parameter

is the Hartmann number

is the Prandtl number

is the Eckert number

In terms of these dimensionless quantities, equation (7) and (8) may be written after dropping all crops for convenience is

(9)

(10)

The initial and boundary conditions for the velocity and temperature profile in the dimensionless form are written as

for  and 			             (11)

for , for 				             (12)

where  is assumed to be the exponential decaying pressure gradient . Equation (9) and (10) represent a system of partial differential equations which is solved numerically under the initial and boundary condition (11) and (12), using the computer code from Maple software for different values of the parameters and . The effects of these parameters are analyzed and discussed graphically. Actually, because the solutions are very large, we will only show the graphical representations of these solutions.

3.  Discussion of the results

Figure 1 and 2 illustrate the time development for velocity  and temperature profile at a very low magnetic field  when  and . The figures are computed for various values at time  when.These figures show that  decreases monotonically with time while increases at a small time and slightly decreases at a large time when . However, with non zero values of ,  further decreases with time for short and long period while temperature reach the steady state at time develops. This is due to increase in the value of  .

Figure 3 and 4 show the time evolution of  at the centers of the channel , respectively for various values of magnetic field parameter  and for .

These figures are computed when. It is clearly show from figure 3 that as the value of parameter increases, decreases and reach its steady state time for all values of . This is because the transverse magnetic field opposes the motion of the fluid. Also, the rate of decreasing in becomes smaller as the value of  increases. This is clear indication that the parameter  has a great effect on the steady state time of  and this effect is more apparent for higher values of .

Figure 4 indicates the effect of parameter on temperature profile . Increasing in slightly increase  at a small times and decreases it at large times until it reach its steady state time at. This is because increase increases the Joule dissipation at small time. But for a large time, increasing  decreases  apparently which in turn decrease the Joule and viscous dissipations. This results for the crossing over of the curves of  when as seen in figure 4 (a). However, with non zero values of  reach the steady state with time for short and long period as shown in figure 4 (b) and (c).

Figure 1: Time variation of the velocity profile  for various values of  and  when ,, ,    and

Figure 2: Time variation of the Temperature profile  for various values of  and  when ,, ,    , , and

Figure 3: Effect of magnetic field parameter on the velocity profile  for various values of  when,,  and

Figure 4: Effect of magnetic field parameter on the Temperature profile  for various values of  when,, , , and

4.  Conclusion

The unsteady flow of a third grade, fluid between two parallel fixed plates is studied. The flow is analyzed under the influence of an applied uniform magnetic field as well as decaying exponential pressure gradient. The effects of magnetic field and third grade parameter on the velocity and temperature profile are analyzed and discussed graphically. It clearly shows that the magnetic field and third grade parameter has a marked on the velocity and temperature profile as the fluid is flowing through the plates. It is interesting to find out that the variation of velocity and temperature with magnetic field and third grade parameter depend on time.

REFERENCES

[1]  Hayat T., Ellah R. and Mahomed F. [2009]. “The Analytical solutions for Magnetohydrodynamic flow of a third order fluid in a porous medium”, J. Naterforsch. 64a, 531-539.

[2]  Siddiqui A.M., Haroon T., Zahid M. and Shahzad A. [2011]. “Effect of Slip condition on unsteady flow of an Oldroyd-B fluid between Parallel plates,” World Applied Sciences Journal 13 (11): 2282-2287.

[3]  Aiyesimi Y.M, Okedayo G.T and Lawal O.W [2014]. “Effects of  Magnetic field on the MHD flow of a third grade fluid through Inclined channel with ohmic heating”, J. Appl. Computat Math 3:153. doi:104192/2168-9679.

[4]  Nayak I., Nayak A.K and Padhy S. [2012], “Numerical solution for the Flow and heat transfer of a third grade fluid part a porous vertical Plate”, Adv. Studies Theor. Phys., vol. 6, 2012, no.13, 615-624.

[5]  Sutton G.W and Sharman A. [1965]. Engineering Magnetohydrodynamics, McGraw Hill, New York.

[6] B.D Coleman and W.Noll [1965]. “An approximation theorem for functional with application in continuum mechanics”. Arch. Rat. Mech. Anal; vol 56, pp. 191-256.

[7]  Rivlin R.S, Ericksen J.L [1995]. “Stress deformation relations for Isotropic materials, J. Rat Mech Impass Anal”, 3:323.

[8]  Schlichtny H. [1986]. “Boundary layer theory, McGraw-Hill, New York

[9]  Attia A.H and Ewis K.M [2010]. “Unsteady MHD couette flow with heat transfer of a viscoelastic fluid under exponential Decaying pressure gradient” Tamkang Journal of Science and Engineering, vol. 13, no. 4, pp. 359-364.