INTEGRATED GEOMORPHOLOGICAL, GEOLOGICAL AND GEOELECTRICAL ASSESSMENT OF THE GROUNDWATER POTENTIAL OF AKURE METROPOLIS, SOUTHWEST NIGERIA

By

Ojo, J.S.1; Olorunfemi, M.O.2; *Akintorinwa, O.J.1; Bayode, S.1; Omosuyi, G.O.1 and Akinluyi, F.O.3

1 Department of Applied Geophysics, The Federal University of Technology, Akure.

2 Department of Geology, Obafemi Awolowo University, Ile-Ife.

3 Department of Remote Sensing and GIS, The Federal University of Technology, Akure.

(*Corresponding Author: orllyola@yahoo.com ojakintorinwa@futa.edu.ng )

ABSTRACT

Geomorphological, geological and geoelectrical data were integrated in the GIS environment to assess the groundwater potential of the Akure Metropolis. The study area is underlain by the Migmatite-Gneiss-Quartzite Complex, Charnockitic and Dioritic rocks, Older Granites and Unmetamorphosed dolerite dykes. Landsat EMT+ surface reflectance image of 2002 of the area were processed to generate geomorphological and lineament maps. Five hundred and thirteen Vertical Electrical Sounding (VES) data set, acquired from 116 localities with the Schlumberger array, were quantitatively interpreted using the partial curve matching technique and computer assisted 1-D forward modeling with W-Geosoft software. The interpretation results (layer resistivities and thicknesses) were used for geoelectrical characterization. Four geomorphological units were delineated. These include residual hills, pediments, low land pediments and etchplain. Satellite-imagery-delineated lineaments show predominantly NNW-SSE, ENE-WSW and NNE-SSW orientations and subsidiary NW-SE and W-E trends that are typical of the Basement Complex region of Nigeria. The VES interpretation results delineate four main subsurface geologic units. These include the topsoil, weathered basement, partly weathered/fractured basement and the fresh basement bedrock. Two major aquifer units - the weathered basement and the partly weathered/fractured basement were delineated though the weathered layer remains the main aquifer unit. Thematic maps of geology, geomorphology, hydro-lineament density, aquifer thickness, and electrical coefficient of anisotropy were integrated to generate the groundwater potential map of Akure Metropolis. The map classifies the metropolis into very low, low, moderate and high groundwater potential zones. Most parts (79%) of the metropolis have very low to low groundwater potential rating (yield of 0.0 - 0.99 l/s) while the groundwater potential rating is at best of moderate level rating (yield of 1.0-1.49 l/s). The high groundwater potential zones are isolated and very limited.

Keywords: Geomorphology, Geology, Geoelectrical Characteristics, Groundwater Potential

INTRODUCTION

Akure, the Ondo State capital, has witnessed rapid housing and estate development, establishment of new industries and expansion of older ones. Population explosion, exacerbated by rural-urban migration, has been accompanied by increase in demand for potable water for human consumption, industrial and agricultural needs. However, access to potable water has remained inadequate because of limited water supply from the Ondo State Water Corporation. The limited water supply is poorly distributed and the distribution networks are poorly maintained. This has led some inhabitants of the metropolis to resort to rainwater harvesting, surface water sources such as streams and rivers and digging of shallow wells. Rivers, streams and shallow hand dug well waters are highly susceptible to contamination through anthropogenic sources. Groundwater is less prone to pollution, requires limited or no treatment and can be developed close to the point of need (Olorunfemi, 2009), which makes it a viable alternative source of potable water. This must have informed the decision of the Ondo State Government, through the Ondo State Water Corporation and the UNICEF Assisted Water Supply and Sanitation Agency (WATSAN), to engage in borehole drilling within the metropolis, as a viable supplement to her inadequate surface water supply scheme.

However, groundwater development in the Basement Complex environment, as is the case in Akure Metropolis, through borehole drilling, has been characterized by spate of failures. Basement aquifers are discontinuous and limited both in lateral and vertical extent (Satpathy and Kanungo, 1976). It is the poor understanding of this hydrogeological characteristics of the Basement Complex environment that is significantly responsible for borehole failures. Secondly, detailed regional assessment of the groundwater potential of the study area has not been undertaken. There is therefore the need to assess the groundwater potential of Akure Metropolis using remote sensing, geomorphological, geological, geoelectrical data and existing borehole information. The research deliverable – a groundwater potential map, will be useful for short and long term planning of groundwater development programme, for the study area.

The hydro-geophysical evaluation of the groundwater potential of Akure Metropolis was carried out by Olorunfemi et al., 1999, using lineament, static water level analysis, limited groundwater yield data and geoelectrical data. The metropolis was broadly classified into low, medium and high groundwater potential zones. The constraint of this study was that sampling points were located based on available topographic map (not georeferenced) and hence may have been subjected to significant spatial error. The data points were limited, so also were the thematic maps. Sampling points in the present study will be properly geo-referenced and the spatial distribution enhanced. Several thematic maps will be synthesized, in a GIS environment, for the development of the groundwater potential map.

Description and Physiography

Akure Metropolis lies within Latitudes 7o 09' and 7o 19'N and Longitudes 5o 07' and 5o 17'E (Northings 790820 – 809277 mN and Eastings 733726 – 752139 mE, UTM Minna Zone 31) (Fig. 1).  The metropolis is located on a gently undulating terrain surrounded by isolated hills and inselbergs. Topographic elevations vary between 260 and 470 m above sea level (Owoyemi, 1996). The metropolis is drained by several streams and rivers. The major ones are Rivers Ala, Ogburugburu and Elegbin and their tributaries.

Geology and Hydrogeology

The area around the Akure Metropolis is underlain by four of the six petrological units of the Basement Complex of southwestern Nigeria as identified by Rahaman (1988). These are the Migmatite-Gneiss-Quartzite Complex, Charnockitic and Dioritic rocks, Older Granites and Unmetamorphosed dolerite dykes (Fig. 2). The study area exhibits varieties of structures such as foliation, schistosity, folds, faults, joints and fractures. Generally, the structural trends in the study area are NNW-SSE and NNE-SSW. Numerous small and long fractures, joints and fissure zones which generally trend north-south are common. These structural trends fall within the principal basement complex fracture direction identified by Oluyide, 1988. Lineaments extracted from aerial photographs, satellite imageries and Side Looking Airborne Radar (RADAR) imageries over Akure area showed that the lineaments predominantly trend in the ENE-WSW direction (Owoyemi, 1996; Odeyemi et al., 1999). The lineament map generated by Owoyemi, 1996 showed high density of lineament and lineament intersections in the eastern, southwestern and north central part of the metropolis underlain by granites and migmatite gneiss while the north central part underlain by charnockites has very low lineament density.

The groundwater, in a typical basement complex area like the Akure Metropolis, is contained in two major aquifer units, namely weathered and fractured basement aquifers (Ako and Olorunfemi, 1989; Aniya and Schoeneick, 1992; Olorunfemi and Fasuyi, 1993; Afolayan et al., 2004 and Bayode et al., 2006). The former is derived from chemical alteration processes while the latter is the product of tectonic activities. The Basement Complex rocks are mostly concealed by a sequence of unconsolidated

Fig. 1: Map of Akure Metropolis – The Study Area, Showing the Topographic Variations

Fig.2: Geological Map of Akure Metropolis (After Owoyemi, 1996)

superficial deposits and basement regolith produced by prolonged weathering of the parent rock. Rocks dominated by unstable ferromagnesian minerals tend to weather into clay, sometimes, micaceous impermeable poor water discharging rock formations while those rocks rich in quartz and other stable minerals will disintegrate into porous and permeable water bearing gravelly or sandy medium (Offodile, 2002).

The weathered layer aquifer may occur singly or in combination with the fractured aquifer. Olorunfemi and Fasuyi (1993) identified the aquifer combinations in the basement complex area as weathered layer aquifer; weathered/fractured (unconfined) aquifer; weathered/fractured (confined) aquifer; weathered/fractured (unconfined)/fractured (confined) aquifer and the fractured confined aquifer. Porosity and permeability determine the storativity and the groundwater yielding capacity of rocks and these characteristics depend on texture and mineralogy of rocks. In fresh, non-fractured crystalline rocks, the porosity is often less than 3% and the permeability is virtually nil. However, the porosity and permeability are increased considerably by weathering and fracturing (Offodile, 2002). Aquifers in the basement rocks are highly limited in lateral and depth extent (Satpathy and Kanungo, 1976).

METHODOLOGY

Geomorphological and Structural (lineament) Mapping

In this study therefore, rock and soil units, topographic profile, streams, rivers and other features were identified and delineated from digital satellite scenes using appropriate software-supported techniques. Subset Topographic map, Aster DEM, Landsat EMT+ surface reflectance image of 2002 of the study area were pre-processed for geometric correction, haze reduction and re-sampling. Optimum index factor and covariance analysis were carried out in order to determine the least correlated bands and these bands were subjected to convolution filters, texture analysis at 3X3 window size, histogram equalization, de-correlation stretch, principal component analysis (PCA) and the Aster DEM to topographic analysis such as sink fill and shielded relief to generate classified land cover, geomorphological and lineament maps.

Geophysical Investigation

The geophysical investigation involved the electrical resistivity method. The Vertical Electrical Sounding (VES) technique adopting a Schlumberger array was used. The half current electrode spacing (AB/2) was varied from 1 m to a maximum of 100 m .The choice of the VES stations was constrained by the geology, structure (lineament) map, terrain, accessibility and representativeness of the spread of the stations. Every VES station was appropriately geo-referenced. Secondary information on existing VES data and borehole records (logs, yield etc.) were assessed re-processed and incorporated. Four Hundred and two (402) Vertical Electrical Sounding (VES) data from 114 localities were sourced and collated. Twenty five (25) sets of borehole data were also sourced. Additional one hundred and eleven (111) primary VES data were collected from Aule and Ilupeju areas of Akure Metropolis where the secondary data were not representative or non-existent. In all, five hundred and thirteen (513) VES data set from 116 localities were acquired. A GPS generated base map with sample locations are shown in Figure 3. The VES data were presented as depth sounding curves and interpreted quantitatively using the partial curve matching technique and computer assisted 1-D forward modeling with W-Geosoft software. The interpretation results (layer resistivities and thicknesses) were used for geoelectrical characterization and computation of electrical coefficient of anisotropy (Olorunfemi et al., 1991).

RESULTS AND DISCUSSION

Geomorphology and Structures (Lineaments)

Figure 4 shows the geomorphological map of the study area. The geomorphological units include residual hills with elevations of 353 – 470 m above sea level (a.s.l.) located at the northern, south central and western flank of the metropolis. The pediments are located at the foot of the residual hills with elevations in the range of 328 – 353 m a.s.l. Both relatively high elevation geomorphological units constitute the water shed for the numerous streams and rivers. The low lands pediments (307 – 328 m a.s.l) and the etchplain (260 – 307 m a.s.l.) fall within and around the stream/river channels and are located at the western/southwestern, southern and eastern flank.  The satellite imagery delineated lineaments are shown in Figure 5. The lineaments show predominantly NNW-SSE, ENE-WSW and NNE-SSW orientations and subsidiary NW-SE and W-E trends that are typical of the Basement Complex region of Nigeria (Oluyide, 1988, Owoyemi, 1996 and Odeyemi et al., 1999).

Geophysical Investigation

(i) Characteristics of the VES Curves

The VES type curves range from 2-layer to three-layer H; four-layer AA, HA, KH and QH; five-layer AKH, HAK, KHA, KQH and QHA and six-layer HKHA, HKQH, KHKH, KQHA and QHKH type (Fig. 6). The KH and H type curves predominate with frequencies of 26% and 24% respectively while the HA and HKH type follow with frequencies of 13% and 11% respectively. The four type curves account for 74% of the total.

Fig. 3: Geophysical (VES) and Borehole Data Acquisition Map

Fig. 4: Geomorphological Map of Akure Metropolis

Fig. 5: Lineament Map of Akure Metropolis

Fig. 6: Histogram of the VES Type Curves.

(ii) Subsurface Geoelectric/Geologic Sequence

The VES interpretation results delineate four main subsurface geologic units. These include the topsoil, weathered basement, partly weathered/fractured basement and the fresh basement bedrock. The topsoil is the uppermost layer which, at some localities, is underlain by a lateritic layer. The layer resistivity values vary widely between 13 ohm-m and 7133 ohm-m (Fig. 7) with the highest frequency of occurrence between 13 and 300 ohm-m. The wide variation in layer resistivity depicts variations in composition degree of fluid saturation (or moisture content) and degree of compaction. The low resistivity (< 300 ohm-m) end of the resistivity spectrum is typical of clay and sandy clay while the high/very high resistivity end (> 300 ohm-m) is diagnostic of clayey sand, sand and laterite. The topsoil thicknesses range in value from 0.3 m to 5.2 m but are generally less than 1.5 m (Fig. 8). The topsoil becomes thicker when it is underlain by a lateritic layer or merges, in resistivity, with the underlying weathered basement.

The weathered layer underlies the topsoil directly in most places unless where the fresh basement rock occurs at shallow depth (nearly outcropping) and it merges with the topsoil or is outcropping. The layer resistivity values range between 6 ohm-m and 727 ohm-m with the highest frequency in the 6-150 ohm-m range (Fig. 9). The weathered layer varies in resistivity and composition depending on the parent rock – typically clayey with low layer resistivity values (< 100 ohm-m) over basic charnockite and sandy/clayey sand (> 100 ohm-m) on fine-coarse grained granitic/gneissic rocks. The weathered layer thicknesses vary between 0.3 m and 106 m (Fig. 10).

The partly weathered/fractured basement column sometime underlie the weathered layer directly (as unconfined fractured basement) (Olorunfemi and Fasuyi, 1993) or occurs within fresh basement rock (as confined fractured basement). This geologic layer was only delineated beneath some VES stations. The layer resistivity values range from 17 ohm-m to 985 ohm-m with the highest frequency in the 17-300 ohm-m range (Fig. 11). The thickness of this horizon varies from 0.2 m to 108 m but is generally less than 25.0 m (Fig. 12).

The fresh basement rock is typically characterized by layer resistivity values greater than 1000 ohm-m. Lower resistivity values (< 1000 ohm-m) were obtained at locations where the overlying layer is very conductive leading to a screening effect and an underestimation of the resistivity of the expectedly infinitely resistive basement rock.

Fig. 7: Histogram of the Topsoil Resistivity.

Fig. 8: Histogram of Topsoil Thickness.

Fig. 9: Histogram of Weathered Layer Resistivity.

Fig. 10: Histogram of Weathered Layer Thickness.

Fig. 11: Histogram of Partly Weathered/Fractured Basement Resistivity.

Fig. 12: Histogram of the Partly Weathered / Fractured Basement Thickness.

(iii)  Basement Structures

Basement structures such as fractures and faults are often discernable from VES curves and usually manifest as inflections on the rising segment of the VES curves (Olorunfemi and Fasuyi, 1993, Olorunfemi, 2009, Ademilua and Olorunfemi, 2011, Ojo and Olorunfemi, 2013a&b). Using the above characteristics to interpret the VES curves, partially weathered/fractured basement columns were delineated in 233 (45.5%) of the 512 VES curves processed. The frequency of occurrence of such basement fractures is however controlled by the geology – much higher in quartzitic and migmatitic gneiss rocks than in charnockite and granite.

(iv) Aquifer Types

Two major aquifer units were delineated in the study area. These include the weathered basement and the partly weathered/fractured basement. The two aquifer units occur in five combinations as observed by Olorunfemi and Fasuyi, 1993. The weathered layer however remains the main aquifer unit.

Groundwater Potential Map

In basement complex terrain, groundwater occurs in weathered and or fractured basement columns (Olorunfemi and Olorunniwo, 1985; Olorunfemi and Fasuyi, 1993; Ariyo and Adeyemi, 2009; Akinluyi, 2013 and Ojo and Olorunfemi, 2013a&b). The effective porosity of these two aquifer units determines the storage capacity whereas the connectivity of the pore spaces and hence the aquifer permeability, determines the groundwater yield. Although the weathered layer is porous, its permeability and hence the groundwater yielding capacity is limited by the clayey nature of the aquifer unit. Fractured basement porosity and permeability are enhanced by fractures and network of joints and shear zones which assist groundwater flow. Basement complex profile with both weathered and fractured basement aquifers usually have characteristically high groundwater yield (Olorunfemi et al., 1993; Olorunfemi, 2008). However, the nature of the weathered basement and the intensity of fracturing is determined by the geology. For example migmatitic and quartzitic rocks have tendency for higher degree of fracturing than metasediments  (schist) and charnockitic rocks (Olorunfemi and Olorunniwo, 1985 and Olorunfemi and Fasuyi, 1993). Most areas underlain by crystalline rocks are characterized by high relief with high run-off and low infiltration (or recharge) rates, making geomorphology a factor in groundwater potential evaluation (Ariyo and Adeyemi, 2009).

Aquifer permeability constitutes the most important hydrogeological parameter in groundwater yield and hence groundwater potential assessment. In basement complex terrain, permeability is aided by faults, fractures and network of joints and shear zones. One of the established means of determining faults, fractures and joints is through lineament mapping from topographical maps, satellite imageries and other remotely sensed imageries. Such generalized lineaments are further processed for hydro-lineaments (lineaments that are hydrogeologically relevant). The degree of fracturing or inhomogeneity can also be established through the determination of electrical coefficient of anisotropy (λ) which has been found to be related to groundwater yield (Olorunfemi et al., 1991).

In this study, thematic maps of geology, geomorphology, hydro-lineament density, aquifer thickness, and electrical coefficient of anisotropy were integrated to generate the groundwater potential map of Akure metropolis. The maps were imported into the GIS for storage followed by the allocation of weight to each layer and different score to each attribute within the layers (Table 1) using reclassification and buffer generation methods. The groundwater potential map was finally composed using overlay function to combine all the layers.

Figure 13 shows the generated groundwater potential map for the Akure Metropolis. The map classified the study area into very low, low, moderate and high groundwater potential zones based on Carruthers and Smith, 1992 and Akinluyi, 2013 groundwater yield-potential classification in a typical basement complex environment.  The map was validated using twenty five geo-referenced borehole groundwater yield data with a 76% correlation between the borehole yield rating and the groundwater potential map rating (Table 2). 3.2% of the survey area (comprising parts of Araromi, Igbatoro, Army Barrack  and Ondo Road) falls within the very low groundwater potential zone with groundwater yield of < 0.5 l/s; 75.8% of the study area comprising Road Block area, Obele, parts of Shagari Estate, Odudu, Fanibi, Akure Stadium, Owena Motel area, Igbatoro, Oshinle, Ijoka, parts of Oke Aro, Adofule, Pelebe Ilekun, School of Agriculture and parts of Benin Garage) falls within the low groundwater potential zone with groundwater yield of 0.5 – 0.99 l/s while 21% 9 comprising of parts of FUTA, Benin Owena River Basin area, Alagbaka, Idita, parts of Obele Estate, north of Adofule, Ijapo Estate etc) falls within the moderate groundwater potential zone with yield of 1.0 – 1.49 l/s and a tiny fraction or 0.03% falls within the high groundwater potential zone (> 1.5 l/s) in the northeastern and south central part.

Table 1: Multi-criteria Evaluation (MCE) Parameters for the Generation of Groundwater Potential Map.

| S/N | Thematic Map (Layer) | Attribute | Rating | Weightage (%) |
| --- | --- | --- | --- | --- |
| 1 | Hydro-lineament , Density | 0 – 0.17 | 1 | 40 |
|  |  | 0.17 – 0.47 | 3 |  |
|  |  | 0.47 – 0.81 | 4 |  |
|  |  | 0.81 – 1.179 | 5 |  |
| 2 | Geology (Lithology) | Charnockite | 1 | 40 |
|  |  | Biotite Granite | 2 |  |
|  |  | Migmatite Gneiss | 3 |  |
|  |  | Porphyritic Granite | 5 |  |
| 3 | Hydro- Geomorphology | Rsidual Hill | 1 | 15 |
|  |  | Pediment | 2 |  |
|  |  | Pediplain | 3 |  |
|  |  | Etchplain | 4 |  |
| 4 | Aquifer Thickness (m) | 0-10 | 1 | 10 |
|  |  | 10-20 | 2 |  |
|  |  | 20-40 | 3 |  |
|  |  | 40-176 | 4 |  |
| 5 | Coefficient of Anisotropy | 1.0-1.12 | 1 | 10 |
|  |  | 1.12-1.19 | 2 |  |
|  |  | 1.19-1.30 | 3 |  |
|  |  | 1.30-2.00 | 4 |  |

Table 2: Validation Parameters for the Groundwater Potential Map

| S/N | Borehole Geographic Co-ordinate | Groundwater Yield/Potential Rating | Rating from Groundwater Potential Map |
| --- | --- | --- | --- |
|  | Northings (m) | Eastings (m) |  |  |
| 1 | 792741.455 | 738424.948 | 0.93 (L) | L |
| 2 | 793126.481 | 739276.377 | 1.20(M) | M |
| 3 | 796356.600 | 742643.191 | 1.20(M) | M |
| 4 | 796867.706 | 744129.232 | 1.20(M) | M |
| 5 | 799067.926 | 744782.074 | 0.75(L) | L |
| 6 | 799522.853 | 740356.969 | 1.26(M) | L |
| 7 | 800294.798 | 741141.960 | 1.12(M) | L |
| 8 | 800618.881 | 747747.666 | 1.00(M) | L |
| 9 | 801511.182 | 744858.545 | 0.50(L) | L |
| 10 | 801780.404 | 743353.525 | 0.75(L) | L |
| 11 | 801810.684 | 743261.315 | 1.14(M) | M |
| 12 | 801967.971 | 740836.250 | 0.50(M) | L |
| 13 | 802357.591 | 748260.774 | 1.23(M) | M |
| 14 | 802725.064 | 741722.525 | 1.26(M) | L |
| 15 | 803236.542 | 739458.474 | 0.90(L) | L |
| 16 | 803654.278 | 749481.846 | 0.89(M) | L |
| 17 | 804140.884 | 748466.734 | 1.10(M) | M |
| 18 | 804160.351 | 739874.441 | 1.10(M) | L |
| 19 | 804240.518 | 743740.482 | 0.80(L) | L |
| 20 | 806054.374 | 737564.021 | 0.80(L) | L |
| 21 | 806085.246 | 737594.558 | 0.20(VL) | L |
| 22 | 806392.947 | 737685.142 | 0.80(L) | L |
| 23 | 807085.737 | 747439.448 | 0.60(L) | L |
| 24 | 807113.114 | 746764.238 | 1.00(M) | M |
| 25 | 807487.338 | 747867.042 | 0.82(L) | L |

VL: Very Low Potential; L: Low Potential; M: Moderate Potential

Fig. 13: Groundwater Potential Map of Akure Metropolis

CONCLUSIONS

Geomorphological, geological and geoelectrical data were integrated in the GIS environment to assess the groundwater potential of the Akure Metropolis. The study area is underlain by the Migmatite-Gneiss-Quartzite Complex, Charnockitic and Dioritic rocks, Older Granites and Unmetamorphosed dolerite dykes.

Subset Topographic map, Aster DEM, Landsat EMT+ surface reflectance image of 2002 of the study area were used to generate geomorphological and lineament maps of the Akure Metropolis. The identified geomorphological units include residual hills, pediments, low land pediments and etchplain. The satellite-imagery-delineated lineaments predominantly trend NNW-SSE, ENE-WSW and NNE-SSW. Five hundred and thirteen (513) VES data set from 116 localities were acquired (primary and secondary), processed and interpreted quantitatively using the partial curve matching technique and computer assisted 1-D forward modeling with W-Geosoft software.

The VES type curves range from 2-layer to three-layer H; four-layer AA, HA, KH and QH; five-layer AKH, HAK, KHA, KQH and QHA and six-layer HKHA, HKQH, KHKH, KQHA and QHKH type. The KH and H type curves predominate with frequencies of 26% and 24% respectively. The VES interpretation results delineate four main subsurface geologic units. These include the topsoil, weathered basement, partly weathered/fractured basement and the fresh basement bedrock. Two major aquifer units were delineated in the study area. These include the weathered basement and the partly weathered/fractured basement. The two aquifer units occur in five combinations as observed by Olorunfemi and Fasuyi, 1993. The weathered layer however remains the main aquifer unit.

Thematic maps of geology, geomorphology, hydro-lineament density, aquifer thickness, and electrical coefficient of anisotropy were integrated to generate the groundwater potential map of Akure Metropolis.

The map classifies the metropolis into very low, low, moderate and high groundwater potential zones. Most parts (79%) of the metropolis have very low to low groundwater potential rating (yield of 0.0 - 0.99 l/s) while the groundwater potential rating is at best of moderate level rating (yield of 1.0-1.49 l/s). The high groundwater potential zones are isolated and very limited.

ACKNOWLEDGEMENT

This research was funded by the Educational Trust Fund (ETF) through the University Research Grant of The Federal University of Technology, Akure. The authors are immensely grateful.

REFERENCES

Ademilua, L.O. and Olorunfemi, M.O. (2011) Further Reflections on Computer Modelling for Detectability Assessment of the transition Zone in the Basement Complex Terrain of Southwest Nigeria. The Pacific Journal of Science and Technology, Vol. 12(1), pp. 435-471.

Afolayan, J.F., Olorunfemi, M.O. and Afolabi, O. (2004) Geoelectric/Electromagnetic VLF Survey for Groundwater Development in a Basement Terrain – A Case Study. Ife Journal of Science, Vol. 6, (i), pp. 74-78.

Akinluyi, F.O. (2013) Integration of Remotely Sensed and Geophysical Data in Groundwater Potential Evaluation of the Basement Complex Terrain of Ondo State, Southwestern Nigeria. Unpublished Ph.D. Thesis, Obafemi Awolowo University, Ile-Ife. 360p.

Ako, B.D. and Olorunfemi, M.O. (1989) Geoelectric Survey for Groundwater in the Newer Basalts of Vom, Plateau State, Journal of Mining and Geology, 25(1), pp. 247-250.

Aniya, F.B and Shoeneick, K. (1992) Hydrogeological Investigation of the Aquifer of Bauchi Area. Journal of Mining and Geology, 28(1), pp. 45-53.

Ariyo, S.O. and Adeyemi, G.o. (2009) Role of electrical resistivity method for groundwater exploration in hard rock areas: A case study from Fidiwo/Ajebo areas of southwestern Nigeria. The Pacific Journal of Science and technology, vol. 10(1), pp. 483-486.

Bayode, S.; Ojo, J.S. and Olorunfemi, M.O. (2006) Geoelectric Characterization of Aquifer Types in the Basement Complex Terrain of Parts of Osun State, Nigeria. Global Journal of Pure and Applied Sciences, 12(3), pp. 377-385.

Carruthers, R.M. and Smith, I.F. (1992) The use of Ground Electrical Survey Methods for Sitting Water Supply Boreholes in Shallow Crystalline Basement Terrains. In Wright, E. R. and Burgess, W.G. (Eds.) The Hydrogeology of Crystalline Basement Aquifers in Africa, pp. 203–220.

Odeyemi, I.B.; Asiwaju-Bello, Y.A. and Anifowose, A.Y.B. (1999) Remote Sensing Fracture Characteristics of the Pan African Granite Batholiths in the Basement Complex of Parts of Southwestern Nigeria. Journal of Techno-Science, vol. 3, pp. 56-60.

Offodile, M.E. (2002) Groundwater Study and Development in Nigeria. Mecon Geology and Engineering Services Ltd., Jos. Nigeria. 453 p.

Ojo, A.O. and Olorunfemi, M.O. (2013a) Resistivity Modelling of Confined Fractured Basement Column for Varying Thicknesses and Depth of Burial. The Pacific Journal of Science and Technology, Vol. 14(1), pp. 464-475.

Ojo, A.O. and Olorunfemi, M.O. (2013b) A Graphical and Semi Quantitative Technique for Investigating Vertical Electrical Sounding (VES) Curves for Indices of Confined Fractured Basement Column. Ife Jounal of Science, Vol. 15(2), pp. 353-366.

Olorunfemi, M.O. (2009) Groundwater Exploration, Borehole Site Selection and Optimum Drill Depth in Basement Complex Terrain. Special Publication series 1. (ISSN 0795-6495). Published by Nigerian Association of Hydrogeologists. 20 pp.

Olorunfemi, M.O. and Fasuyi, S.A. (1993) Aquifer Types and the Geoelectric/Hydrogeologic Characteristics of Part of the Central Basement Terrain of Nigeria (Niger State).  Journal of African Earth Sciences, vol. 16, no. 3, pp. 309-317.

Olorunfemi, M.O.; Ojo, J.S. and Akintunde, M.O. (1999) Hydro-Geophysical Evaluation of the Groundwater Potential of the Akure Metropolis, Southwestern Nigeria. Journal of Mining and Geology, vol. 35(2), pp. 207 – 229.

Olorunfemi, M.O.; Ojo, J.S.; Idornigie, A.I. and Oyetoran, W.E. (2005) Geophysical Investigation of Structural Failure at a Factory Site in Asaba Area, Southern Nigeria. Journal of Mining and Geology, 41(1), pp. 111-121.

Olorunfemi, M.O.; Olarewaju, V.O. and Alade, O. (1991) On the electrical anisotropy and groundwater yield in a Basement Complex area of S.W. Nigeria. Journal of African Earth Sciences, Vol. 12(3), pp. 467-472.

Olorunfemi, M.O. and Olorunniwo, M.A. (1985) Geoelecctric parameters and aquifer characteristics of some parts of southwestern Nigeria. Geologia Applicata E. Idrogeologia, vol. xx, pp. 99-109.

Oluyide, P.O. (1988) Structural trends in Nigeria Basement Complex. In Precambrian Geology of Nigeria by P.O. Oluyide (ed.). Geological Survey oof Nigeria Publication, pp. 93-98.

Owoyemi, F.B. 1996. A Geologic-geophysical Investigation of Rain-induced Erosional Features in Akure Metropolis. Unpublished M.Sc. Thesis, Federal University of Technology, Akure. pp. 11 – 18.

Rahaman, M.A. (1988) Recent Advances in the Study of the Basement Complex of Nigeria. In Oluyide, P.O., Mbonu, W.C, Ogezi, A.E., Egbuniwe, I.G., Ajibade, A.C. and Umeji, A.C. (Eds.). Precambrian Geology of Nigeria. Geological Survey of Nigeria Special Publication,  pp. 11-41.

Satpathy, B.N. and Kanungo, D.N. (1976) Groundwater Exploration in Hard Rock Terrain – A Case History. Geophysical Prospecting, vol. 2(4), pp. 725-736.